## Slide 1: POPE and PaNeL
H B Acharya

## Slide 2: Motivation: The Bottleneck
S. Keshav : the rate limiting step in Internet backbones is deciding which action to perform on an arriving packet
  Policies in routers and middleboxes consist of rules; the challenge is to quickly decide which rule applies
To increase throughput, we match different packets in parallel
  But this still requires the latency of checking all the rules

## Slide 3: Parallel = Fast?
Concurrency simply means there is not a serializing causal dependency – things can happen in any order
Parallelism means things actually happen at the same time
Policies are sequential: there is an order of precedence for the rules in a policy.
Can they be evaluated in parallel (without an O(n) wait?)

## Slide 4: Contents
Packets and Rules
Matching and Resolution
XMT
Parallel Resolution
  starring Prefix-Sum
POPE and PaNeL

## Slide 5: Packets and Rules
Decisions on packets are made based on the header values
  Source and Destination address and port, protocol, etc.
  These values are represented by integers
We represent a packet by a tuple of d integers
  Each representing a field of interest, e.g. source IP
  An example packet might be <7, 918, 4, 5, 14>
A rule consists of two components
  A guard: d integer intervals (one for each field)
  A decision specifying an action to take, eg. accept, discard

## Slide 6: The Matching of Packets
A rule matches a packet if
  for all d fields,
  the value specified by the packet lies in the corresponding interval specified in the rule.
For example, the rule <[10, 100], [0, 255]> -> discard matches the packet <51, 0> and not <101, 0>

## Slide 7: Policies and Rule Precedence
Practical policies can be large and complex
  A routing table of 10^5 rules is not unusual
These rules can overlap
  When multiple rules match the same packet, which applies?
  Rule precedence!

## Slide 8: The order of rules
In practice, the order of rules is quite complex
The rule with the “best” match (the smallest specified interval) among the matching rules wins
To break ties, rules are ordered as follows
  Static routes
  Dynamic routes, in order
    the usual order is EIGRP, OSPF, ISIS, RIP
  Default routes

## Slide 9: Introducing XMT
Serial computation: von Neumann machine
  all memory accesses (from the one processor) occur at once
  an instruction, available for execution, executes immediately
Parallel computation: PRAM
  all memory accesses, from any processor, occur at once
XMT is a PRAM-like machine
  many instructions, available for execution, execute immediately, in parallel

## Slide 10: Why XMT?
O(1) Random Memory Access from any processor
Many Core Architecture (1024 cores) leads to better speedup.
Simple and efficient architecture: each Thread Control Unit (core) runs a thread independent of the others
The XMT-C programming language is simple

## Slide 11: Matching Rules in Parallel
Spawn a thread for each rule in the policy (in parallel)
The thread corresponding to a rule checks whether that rule matches the packet or not
In O(1) time [or more accurately O(d) if we check d fields] we find, for each rule, whether it matches the incoming packet

## Slide 12: The Precedence Problem!
For a rule to match a packet is NOT enough!
When multiple rules match a packet (and have different actions) the conflict is resolved using match semantics
  We use first-match semantics: the first rule to match a packet is the one applied.
  This rule is said to resolve the packet
Serial checking: stop after the first rule matches the packet
Parallel checking: how to tell first match?

## Slide 13: Restating the First Match problem
Consider an array A[n]
Each value of the array corresponds to a rule in the policy
  A[i] = 1 iff rule i matches the packet
  A[i] = 0 otherwise
Finding the first rule to match the packet reduces to finding the smallest i s.t. A[i] = 1

## Slide 14: First Match with Prefix Sums
There exists a standard algorithm to compute prefix match of an array of n elements in O(log n)
  Prefix sum A+ of array A is an array of length n, such that A+[i] = A[1]+A[2] + … A[i]
For the first i such that A[i] = 1, A+[i] = 1 also
This is true only for this element.
  Therefore, we can resolve packets in O(1) + O(log n) + O(1) time rather than O(n) time, thanks to the O(log n) prefix-sum algorithm.

## Slide 15: First Attempt : POPE
For every rule in parallel, try to match the packet and store the result of the attempt in corresponding space in A.
Each value of the array corresponds to a rule in the policy
  A[i] = 1 iff rule i matches the packet
  A[i] = 0 otherwise
Compute A+, the prefix sum of A
Perform the action of the rule no. i where A[i] == A+[i] == 1

## Slide 16: Scaling Problems
POPE works very well for small policies
However, the performance drops off for larger policies (say of the order of 104 rules and above)
The reason is simple: POPE always checks ALL the rules
  Whereas serial resolution stops after the first match … which in a large policy, is likely to happen “early,” i.e. in rules high up in the policy

## Slide 17: Second Attempt: PaNeL
Divide large policies up into “batches” of rules
  We find experimentally that batches of 1000 rules work best
  Probably because XMT had 1024 cores?
Perform the POPE algorithm batch by batch, until the first match is found. (One batch at a time)
This reduces the average running time, though not the worst case

## Slide 18: Results

## Slide 19: To Do
Compare the performance of parallelizing rule matching of packets versus the solution of matching multiple packets in parallel.
  Perhaps combine both approaches
The performance seems to vary with the “width index” – the bit width of the fields tested. Further study is indicated

## Slide 20: Q & A

## Slide 21: Prefix Sum
1 2 3 4 3 7 10
1 2 3 4 3 10 10

## Slide 22: Prefix Sum
1 3 3 10 3 10 10
1 3 6 10 3 10 10